## Slide 1: Tetris
Rupp Arian Lampert Mathias

## Slide 2: Projekt-Übersicht
Ziel: - Vollständiges Tetris-Spiel auf ESP32-S3 - LED-Matrix + OLED Hardware: - ESP32-S3 - WS2812B 16x24 - SSD1306 OLED - 4 Buttons Software: - ESP-IDF, FreeRTOS - C (~2000 Zeilen)

## Slide 3: Ursprüngliche Planung
Core Features: - Tetrominos + Rotation - Kollision - Zeilen-Clear - Rendering - Controls Nice-to-have: - WiFi - Webserver - Preview - Pause Zeitplan: Geplant: 3 Wochen Tatsächlich: 4 Wochen

## Slide 4: Architektur
System-Design: - GameLoop - Controls - Grid - Blocks - Score - Display & LEDs

## Slide 5: Code 4.1 ISR
// ISR: Minimale Verarbeitung, nur Queue Push static void IRAM_ATTR gpio_isr_handler(void *arg) { gpio_num_t gpio = (gpio_num_t)(intptr_t)arg; BaseType_t xHigherPriorityTaskWoken = pdFALSE; xQueueSendFromISR(s_button_queue, &gpio, &xHigherPriorityTaskWoken); if (xHigherPriorityTaskWoken) { portYIELD_FROM_ISR(); } }

## Slide 6: Code 4.1 Debounce
bool controls_get_event(gpio_num_t *out_gpio) { gpio_num_t g; if (xQueueReceive(s_button_queue, &g, 0) == pdTRUE) { uint32_t now = xTaskGetTickCount() * portTICK_PERIOD_MS; if (now - last_pressed[g] > BUTTON_DEBOUNCE_MS) { last_pressed[g] = now; *out_gpio = g; return true; } } return false; }

## Slide 7: Kollisionserkennung
bool grid_check_collision(const TetrisBlock *block) { for (int by = 0; by < 4; by++) { for (int bx = 0; bx < 4; bx++) { if (block->shape[by][bx] == 0) continue; int gx = block->x + bx; int gy = block->y + by; if (gx < 0 || gx >= GRID_WIDTH) return true; if (gy >= GRID_HEIGHT) return true; if (gy < 0) continue; if (grid[gy][gx] != 0) return true; } } return false; }

## Slide 8: Delta-Rendering 1
void render_grid() { for (int i = 0; i < prev_dynamic_count; i++) { int pos = prev_dynamic_pos[i]; int y = pos / GRID_WIDTH; int x = pos % GRID_WIDTH; if (grid[y][x] > 0) { uint8_t r, g, b; get_block_rgb(grid[y][x] - 1, &r, &g, &b); led_strip_set_pixel(led_num, r, g, b); } else { led_strip_set_pixel(led_num, 0, 0, 0); } }

## Slide 9: Delta-Rendering 2
int dynamic_count = 0; for (int by = 0; by < 4; by++) { for (int bx = 0; bx < 4; bx++) { if (current_block.shape[by][bx] == 0) continue; int gx = current_block.x + bx; int gy = current_block.y + by; uint8_t r, g, b; get_block_rgb(current_block.color, &r, &g, &b); r = (r * BRIGHTNESS_SCALE) / 255; g = (g * BRIGHTNESS_SCALE) / 255; b = (b * BRIGHTNESS_SCALE) / 255; led_strip_set_pixel(led_num, r, g, b); prev_dynamic_pos[dynamic_count++] = gy * GRID_WIDTH + gx; } } prev_dynamic_count = dynamic_count;

## Slide 10: Delta-Rendering 3
led_strip_refresh(); }

## Slide 11: Clear Rows 1
void grid_clear_full_rows() { int full_rows[4]; int remove_count = 0; for (int y = 0; y < GRID_HEIGHT; y++) { bool full = true; for (int x = 0; x < GRID_WIDTH; x++) { if (grid[y][x] == 0) { full = false; break; } } if (full) full_rows[remove_count++] = y; } if (remove_count == 0) return;

## Slide 12: Clear Rows 2
for (int blink = 0; blink < 2; blink++) { for (int i = 0; i < remove_count; i++) { int y = full_rows[i]; for (int x = 0; x < GRID_WIDTH; x++) { led_strip_set_pixel(led_num, 255, 255, 255); } } led_strip_refresh(); vTaskDelay(pdMS_TO_TICKS(150)); } for (int i = 0; i < remove_count; i++) { for (int x = 0; x < GRID_WIDTH; x++) { grid[full_rows[i]][x] = 0; } }

## Slide 13: Clear Rows 3
for (int x = 0; x < GRID_WIDTH; x++) { int target_y = GRID_HEIGHT - 1; for (int y = GRID_HEIGHT - 1; y >= 0; y--) { if (grid[y][x] != 0) { grid[target_y][x] = grid[y][x]; if (target_y != y) grid[y][x] = 0; target_y--; } } } score_add_lines(remove_count); speed_manager_update_score(total_lines_cleared); }